## Slide 1: Task:
To identify crack on an object using Image processing.
Reference image chosen
Background
Metallic object
Crack to be identified

## Slide 2: Process:
Read the image
Pre-processing
Extract the ROI(metallic object)
Processing ROI
Extract interested
Objects(Cracks)
Resizing, Grayscale , Blurring
OpenCV
Canny edge detector, Morphological operations
and Contour functions
Morphological operations
Canny edge detector and Contour functions

## Slide 3: Image Snippets:
1. Actual Image
2. Grayscale Image
3. Gaussian blur Image
4. Canny edge detection
5. Morphological operations
6. Extracted ROI

## Slide 4: Image Snippets:
7. ROI
8. Morphed ROI
9.Contours detected
Actual output

## Slide 5: Result:
Simple method to Identify Cracks on the metallic plate
Tested positive on image set with test-cases like:
When the position of the metallic object is changed in the image
When the Crack position moves in the image
When multiple cracks are found in the image
Can be easily extended to practical applications with minor changes
Better results when compared with template matching

## Slide 6
Thank you!!